## Slide 1
Feature | WyreStorm NHD-510-TX | AVPro Edge AC-MXNET-1G-EV2 | Lightware GVN-TX-UC | Extron NAV E 222
Product Type | AV over IP Encoder (TX); HDMI + USB-C inputs; pairs with NHD-500 RX | AV over IP Encoder (HDMI only); pairs with AC-MXNET-1G-DV2 | AV over IP Encoder (TX); HDMI + USB-C auto-switch inputs | AV over IP Switching Encoder; HDMI + USB-C (DisplayPort Alt Mode)
Codec | JPEG 2000 — visually lossless | JPEG 2000 — 200–850 Mbps adaptive | Proprietary codec — visually lossless; not JPEG 2000 | PURE3® — wavelet-based lossless (Extron proprietary)
Max Video Resolution | 4K60 4:4:4 8-bit; HDR up to 12-bit 4:2:2 | 4K60 4:4:4 RGB/YCbCr 10/12-bit | 4K60 4:4:4 | 4K60 4:4:4
HDR Support | Dolby Vision, HDR10, HLG | Dolby Vision (≤30Hz), HDR10, HDR10+, HLG | Dolby Vision, HDR10; full HDMI 2.0 HDR support | Full HDMI 2.0 HDR — HDR10, HDR10+, Dolby Vision, HLG
Latency | <1 frame (16ms); 4ms ULLM passthrough mode | ~1 frame (16ms); ULLM mode <4ms; Genlock supported | <1 frame — less than one video frame end-to-end | Ultra-low latency — specific figure not published for 1G
Network (1G) | 1GbE — standard managed switch | 1GbE — Cat6a recommended; MXNet or compatible L3 switches preferred | 1GbE — standard managed switch; CAT copper up to 100m | 1GbE — standard managed switch; IGMP multicast required
Fiber Connectivity | Yes — SFP: 300m OM3 fiber (fiber cabling required) | Yes — SFP fiber option (SFP module required) | Yes — SFP cage: MM up to 550m; SM up to 80km | No — NAV E 222 copper only; fiber not specified
PoE Powered | No — external PSU | No — fanless ~7W, external PSU | Yes — TX: PoE 802.3af powered; RX requires PoE+ | Yes — PoE+ powered (IEEE 802.3at)
Video Wall Support | Up to 16×16 (256 displays); mosaic & rotation | Up to 64 panels/wall; unlimited walls; Genlock sync | Supported via GVN ecosystem; managed centrally through MMU | Supported via NAV platform; NAVigator endpoint management
USB-C Input | Yes — auto-switch HDMI/USB-C; up to 7 USB devices; KVM routing | No — HDMI only on EV2; no USB-C input | Yes — USB-C 100W charging; auto-switch HDMI/USB-C; USB 2.0 data | Yes — USB-C DisplayPort Alt Mode; 100W (with UPI 100 inserter)
Audio | HDMI, Toslink; Dante AV-A 2×2 channels (license required) | Dolby Atmos, DTS:X IMAX Enhanced; no native Dante | HDMI 2.0 audio (7.1 LPCM, Atmos, DTS:X); analog I/O; DNT adds Dante | HDMI embedded audio; AES67 audio over IP standard
Control | WebUI / API, RS-232, NHD-CTL-PRO controller, SYGMA cloud | RS-232, IR; MXNet Mentor software; OLED status display | MMU (Matrix Management Unit) web UI; auto-discovery; EDID management | NAVigator System Manager; embedded WebUI; RS-232 via control system
HDCP | 2.2 / 2.3 | 2.2 / 2.3 (HDCP compliant) | HDCP compliant (version not published) | HDCP compliant (version not published)
Open Switch Ecosystem | Yes — any standard 1G managed switch | Partial — compatible L3 multicast switch required; MXNet preferred | Yes — standard 1G managed switch; no proprietary switch needed | Yes — standard managed switch; IGMP multicast required
Best Stand-Out Point | JPEG2000 + USB-C auto-switch + HDMI loop out + Fiber + Dante AV-A + SYGMA cloud — most versatile 500-series encoder | Proprietary ASIC + Genlock; ULLM <4ms; OLED display; but no USB-C input | PoE TX + USB-C 100W + SFP fiber + MMU management; Dante in DNT variant only | PURE3 lossless + AES67 + USB-C 100W + 1G/10G interoperability + enterprise-scale
WyreStorm NHD-510-TX
Competitive Comparison
WyreStorm Best Positioning
The NHD-510-TX is WyreStorm’s most versatile 500-series encoder, adding USB-C + HDMI auto-switching and HDMI loop-out to the proven JPEG 2000 / SYGMA / Fiber / Dante AV-A platform.
Key strengths:
JPEG 2000 visually lossless quality — same codec trusted by digital cinema
USB-C + HDMI auto-switching — true BYOD with one cable for modern meeting rooms
HDMI loop-out — connect a local display without extra cabling
Dante AV-A — license required; bridges professional audio networks
SYGMA Cloud + open ecosystem — no lock-in, remote management anywhere
Against AVPro Edge EV2: NHD-510-TX adds USB-C input, HDMI loop-out, native Fiber SFP, Dante AV-A, and SYGMA Cloud. EV2 is HDMI-only and pushes toward proprietary MXNet switches.
Against Lightware GVN-TX-UC: Both offer USB-C + SFP fiber. NHD-510-TX leads with JPEG 2000 quality and SYGMA Cloud management, while Lightware offers PoE TX power.
Against Extron NAV E 222: NAV E 222 matches USB-C 100W and enterprise scalability, but uses PURE3 proprietary codec, has no Fiber SFP, and locks into the NAVigator ecosystem. NHD-510-TX offers JPEG 2000, Fiber, Dante AV-A, and SYGMA Cloud.
Summary: Position NHD-510-TX as the upgrade path for modern BYOD environments, combining the proven NHD-500 platform with USB-C auto-switching and HDMI loop-out, while competitors either lack USB-C, require Dante upgrades, or rely on proprietary ecosystems.