## Slide 1
Feature | WyreStorm MX-1007-HYB / MX-0804-EDC | Extron DTP3 CrossPoint Series | Kramer MTX3-88-PR-PRO
Product Type | Hybrid Matrix; 10×7 (MX-1007-HYB) or 8×4 (MX-0804-EDC); 1RU all-in-one | Configurable Matrix Switcher (6×6 to 8×4); HDMI + DTP3 twisted pair; 2U rack | 8×8 All-in-One Hybrid Matrix; USB-C, HDMI, HDBaseT 3.0; H.264/H.265 stream out; 3U
Signal Transport | Uncompressed HDMI + HDBaseT 3.0 local; NHD 500 IP output for AV over IP expansion | Uncompressed — DTP3 over shielded CAT 6A; maximum signal fidelity; zero IP compression | Uncompressed HDMI + HDBaseT 3.0; H.264/H.265 network stream output (not full AV over IP)
Max Video Resolution | 4K60 — built-in scaler 480p to 2160p on all outputs; NHD 500 output: 4K60 4:4:4 | 4K60 4:4:4 — all resolutions uncompressed; Extron Vector 4K scaling on all outputs | 4K60 4:4:4, 18 Gbps; ProScale™ high-resolution scaling engine on all outputs
HDR Support | Full HDMI 2.0 HDR — Dolby Vision, HDR10, HLG | HDR, Deep Color 12-bit; HDMI 2.0b (18 Gbps); Dolby Vision, HLG | Full HDMI 2.0 HDR; HDCP 2.3; 4K60 4:4:4 on all inputs and outputs
Switching Latency | Fast <1 second local switching (HDMI / HDBaseT); NHD IP switching <1s | Ultra-low — uncompressed DTP3 transport; seamless switching via Vector 4K engine | Fast <1 second clean switching; near-zero latency local uncompressed routing
Extension Range | HDBaseT 3.0 up to 100m (MX-1007-HYB); NHD 500 output for unlimited 1G IP reach | DTP3 over shielded CAT 6A — up to 330ft (100m); uncompressed at every resolution | HDBaseT 3.0 — up to 100m over CAT cable; 8 bidirectional configurable ports
AV over IP | Partial — NHD 500 output enables full AV over IP scalability over 1G network | No — proprietary DTP3 twisted pair only; no AV over IP matrix distribution | Partial — H.264/H.265 streaming output only; not a true AV over IP matrix
USB-C + Power | Yes — USB-C: 4K60, USB3.0/2.0, 1G network, PD3.0 up to 60W charging | Via separate DTP3 T 203 transmitter (60W); CrossPoint 642 itself has no USB-C port | Yes — USB-C with 60W charging; MST on first 2 inputs; 6 local USB-A device ports
Video Wall / Multiview | Via NHD 500 IP — up to 16×16 (256 screens); mosaic & rotation via NHD Touch app | Via XTP CrossPoint integration; Vector 4K; logo keying; seamless transition effects | Yes — dual independent video wall + PiP, quad, split-screen multiview layouts
USB Routing / KVM | Yes — USB3.0 host switching; local USB-A device ports; KVM via NHD 500 IP routing | USB 2.0 extension over DTP3 links; remote USB host access to devices at endpoints | Yes — 6 local USB device ports; independent AV + USB routing; USB-follow-AV mode
Audio: Dante + Amp | Dante 4×4 integrated; 100W amp + DSP (MX-1007-HYB); DSP + balanced audio (MX-0804-EDC) | Dante + AES67 (CrossPoint 642); Extron ProDSP with AEC; power amplifier option | Dante + AES67; dual-zone power amplifier; full DSP with AEC + noise filtering
Control | WebUI / API, RS-232, NHD-CTL-PRO controller, SYGMA cloud (free) | Ethernet, RS-232, SIS commands; Extron GCP; ConfigTool software; built-in web server | RS-232, GPIO, Ethernet, relays; OWASP-grade security; Kramer Control integration
HDCP | 2.3 | 2.3 | 2.3
Open Infrastructure | Yes — any standard 1G managed switch; SYGMA cloud; open NHD 500 ecosystem | No — proprietary DTP3/XTP ecosystem; requires matching Extron hardware throughout | No — requires Kramer Series 3 (EXT3/SWT3) endpoints for full HDBaseT ecosystem
Best Stand-Out Point | USB-C 60W + HDBT local + NHD IP scalability + 100W amp + Dante 4×4 + SYGMA cloud | Uncompressed at all resolutions over CAT 6A; Vector 4K + ProDSP + AEC; Extron-deep integration | 8×8 all-in-one powerhouse; USB-C 60W + HDBT 3.0 + Dante + Dual amp/DSP + dual video wall
WyreStorm MX-1007-HYB / MX-0804-EDC
Competitive Comparison
Positioning Angle
The MX-1007-HYB and MX-0804-EDC are WyreStorm’s all-in-one hybrid matrix switchers for modern education and corporate spaces, combining local HDBaseT switching with the scalability of NetworkHD 500 AV over IP.
Hybrid matrix + AV over IP scalability
Start with local HDBaseT switching, then expand to NetworkHD 500 endpoints when more displays, overflow spaces, or wider distribution are needed.
NetworkHD 500 IP output
Bridges traditional matrix switching with genuine AV over IP, allowing systems to scale without replacing the core hardware.
Free SYGMA Cloud management
Enables remote monitoring, firmware updates, and device management from anywhere, helping reduce site visits and simplify long-term support.
Built-in audio value on MX-1007-HYB
A 100W amplifier and Dante 4×4 audio reduce the need for separate DSP or amplifier hardware, saving rack space and lowering system cost.
USB-C, HDMI, and HDBaseT connectivity
Supports modern BYOD workflows with flexible input options for laptops, room PCs, and other presentation sources.
Open 1Gb network infrastructure
NetworkHD 500 runs over standard managed switches, giving integrators more flexibility without being locked into a proprietary network ecosystem.
Against traditional HDBaseT matrix platforms: WyreStorm’s advantage is that the system does not stop at the room. It combines local switching, AV over IP scalability, cloud management, and flexible BYOD in one ecosystem.
For internal use — competitor data sourced from publicly available product pages. Verify specifications before customer-facing use.